## Slide 1: Reducing Air Traffic Delays in Los Angeles
Jerry Chen
Jules Pommies
John Stuart
Brian Tam
Jonathan Wegleitner
University of California, Berkeley
December 2016
Notes: Everyone. Jerry to say title

## Slide 2: Intro: Los Angeles
The Los Angeles Area is one of the busiest air traffic regions in the world
  Population: 18 million (2nd largest in US)
Commercial air service from 5 airports: LAX, SNA, LGB, ONT, BUR
  Of these, LAX by far serves the most destinations and has the greatest frequency of commercial flights
  The 4 other airports almost exclusively serve domestic destinations
LAX is often preferred due to high frequency of flights and more non-stop destinations
However, LAX has many problems including delays and efficiency
Notes: Jerry

## Slide 3: Intro: LAX
From 2010 to 2016, LAX ranked as #1 for the longest delay in taxi-in time
  Closely spaced terminals allow only one aircraft on the apron taxiway at a time
  Closely spaced taxiways can restrict ground aircraft movement
  Taxiway weight restrictions result in longer taxi times
  Almost constant construction results in runway and taxiway closures
Horseshoe terminal layout makes inter-terminal transitions difficult
Los Angeles road traffic makes LAX difficult to get to
LAX is bounded in all 4 directions and almost impossible to expand
Notes: Jerry

## Slide 4: Intro: LA Area Airports
The 4 other LA Area airports are far away from operating near capacity
Airline service already exists at these airports:
  SNA serves over 20 destinations through 7 carriers
  LGB serves about 15 destinations through 4 carriers
  ONT serves about 15 destinations through 7 carriers
  BUR serves about 13 destinations through 6 carriers
These airports are located around the Los Angeles Area
Notes: Jery

## Slide 5: Intro: LA Area Airports
However, these airports carry curfews and restrictions
SNA has night curfews with operations prohibited between 11PM and 7AM
  Especially noisy aircraft are also prohibited from flying to the airport
LGB has noise and flight restrictions, but no curfew
BUR has noise restrictions and curfew on especially noisy aircraft
ONT has no explicit noise restrictions or curfew in place
These airports’ runways may not accommodate very large aircraft
Notes: Jerry

## Slide 6: Motivation
Aircraft delays are costly, inefficient, and unpleasant
  Airlines must pay more for crew time, fuel, and other resources
  Additional airline costs if delay causes missed connections
  Interferes with airport departure slots and can cause ripple effect
  Generates unnecessary noise and fuel pollution
  Creates stress for travelers
Air traffic delays affect everybody, especially at a scale such as LAX
  Travelers
  Ground Transportation
  Pilots, Flight Attendants, Airline and Airport Ground Service Agents
  Air Traffic Controllers
Notes: Jerry

## Slide 7: Research Question
How can these delays be reduced?
Proposed Solution: Redistribute air traffic among LA Area airports
  Forced market - flights no longer offered based on demand
  Scheduled flights are assigned based on how congested LAX is at a particular time of day
  Sole criteria for redistribution: reducing the ground delay at LAX
Additional Considerations
  Reduced delay will reduce environmental, operational costs
  Travelers must receive incentives for loss of convenience
Notes: Jerry

## Slide 8: Broad Theory
LAX is not always congested to extreme degrees
  Most notable delays in later morning and later afternoon rushes
Travelers are generally flexible
  Passengers are already willing to pay more for airfare from other airports because of better travel experience
  Relatively few travelers live exclusively close to a certain airport
Demand is steady and increasing to other airports
Costs of loss of free market do not outweigh benefits of better efficiency
Notes: Jerry

## Slide 9: Background: Five Major Airports LAX John Wayne Ontario Bob Hope Long Beach
Notes: Brian

## Slide 10: Location: Five Major Airports
Notes: Brian

## Slide 11: Opportunity to Improve
DEN
Notes: Jack - Background stats
Brian - Capacity visualization

## Slide 12
LAX
LGB
Notes: Brian

## Slide 13: LAX Approach and departure paths
Notes: Jack

## Slide 14: John Wayne / Long Beach Trip
Notes: Brian

## Slide 15
Notes: Brian

## Slide 16
Notes: Brian

## Slide 17: Forced market: Can we make this more optimal?
Notes: Brian

## Slide 18: Methodology
Research Question
Background Research
Obtain Data
Data Visualization
Program Development
MILP
Dynamic Program
Landside Analysis
Implementation
Suggested Implementation
Notes: Jack

## Slide 19: Existing Air Service System
Airports offer slots to airlines, which set a maximum on airline service
  May be bounded by number of flights, or number of passengers
  Are distributed to airlines according to legal procedures
  Slots can be as restrictive as they need to be
Airlines schedule flights in accordance with their slot allocations
  Generally, slots dictate how many gates are available
  Airlines try to schedule flights to meet service demand
Airports are competitors, and generally operate independent of another
  Exceptions for when departure paths cross, or other factors
Notes: Jack

## Slide 20: Data Categories
Carrier
Airport
Flight Plan Gate Out
Actual Gate Out
Flight Plan Gate In
Actual Gate In
Unimpeded Taxi Out Time
Taxi Out Time
Taxi Out Time Difference
Taxi Out Delay
Estimated Time Enroute
Tail Number
ACID
Actual Airborne Time
Airborne Time Difference
Airborne Delay
Unimpeded Taxi In Time
Taxi In Time
Taxi In Time Difference
Taxi In Delay
Scheduled Block Time
Actual Block Time
Block Time Difference
Block Delay
Departure
Arrival
Notes: Jack
Aviation System Performance Metrics (ASPM)

## Slide 21: Initial Data Interpretation Southwest Airlines
Notes: Jack

## Slide 22: Initial Data Interpretation Southwest Airlines
Notes: Jack

## Slide 23: Initial Data Interpretation American Airlines
Notes: Jack

## Slide 24: Initial Data Interpretation American Airlines
Notes: Jack

## Slide 25: Modeling - Two Approaches
Mixed Integer Linear Programming
Uses linear programming and branch and bound algorithm to optimize
Easy to implement and change
Very time inefficient for large numbers of aircraft
Time complexity unpredictable for difficult scenarios
Dynamic Programming
Uses recursion to map optimal solutions
Complicated to implement
Theoretically less computationally intensive as MILP, with more predictable time complexity
Difficult to change constraints
Notes: John

## Slide 26: Approach 1 - MILP
Minimizes the sum of difference between an aircraft’s earliest possible arrival time and new scheduled time
Imposes limit on delay of any one aircraft
Imposes FAA separation requirements on aircraft approaching the same runway.
Notes: Jon

## Slide 27: Assumptions
The MILP makes a number of permissible assumptions about aircraft dynamics and regulations to enable faster computation.
Schedules repeat over the course of days or weeks.
7 Runways for arrivals (2 each at LAX and LGB).
Aircraft arrive from 4 general directions, meaning additional flight time to each airport varies.
Once at an airport, all aircraft merge into a single approach path
Temporarily Relaxed Details:
Runway capabilities (based on weight class)
Variable headway requirements (an average of 90 seconds used)
Actual vs random origin direction
Notes: John

## Slide 28: Constraint Selection
Additional function (LongTermPlot.m) developed to explore the effect of constraints on delay
Looping over different scheduling window limits and available airport constraints, we can determine feasible constraints graphically.
Generated plots show the delay reduction effect of scheduling over a larger sample of airports.
LongTermPlot also graphs cumulative rerouting decisions from each sample set
Notes: John

## Slide 29: Output of Bivariate Constraint Program - (LongTermPlot.m)
Notes: John

## Slide 30: Implementation
Individual flight data is extracted from ASPM database
Aircraft equipment ID and other databases are used to determine: ➤ weight category ➤ fuel consumption ➤ point of origin ➤ original destination, ➤ separation requirements ➤ time impacts of changing destination
For loops assemble the constraint arrays A, B, Aeq, and beq from the data calculated in Step 2
Intlinprog function uses the simplex algorithm and branch and bound to explore options and find a delay minimizing schedule
Notes: John

## Slide 31: Results
Every iteration generates a plot of runway decisions and a complete schedule vector.
Originally sample sizes were too small to produce meaningful results. Most results would be either infeasible or have zero delay
Proper selection of a scheduling window solves this problem
Notes: John - Proper scheduling windows also generate

## Slide 32: Approach 2 - Dynamic
Dynamic programming takes a desired final state and systematically explores all possible ways of minimizing cost of reaching that state.
Previous work has been done on using dynamic programming to maximize minimum separation in air traffic (Bayen et al 2004) but minimizing delay takes a new approach.
This dynamic program seeks to pack “aircraft blocks” or windows of landing time and headway, into as small a timespan as possible.
Notes: John

## Slide 33: Issues and Improvements
MILP
Time efficiency has been improved with random points of origin and reducing the aircraft sample size
Number of variables increases polynomially, unknown O(f(N))
LongTermPlot.m function has provided optimal constraint combinations to try
Attempt iteration over entire day with
Dynamic
Additional debugging required
Notes: John

## Slide 34: LAND-SIDE
Notes: Jules

## Slide 35: LAX Survey
Notes: Jules

## Slide 36: Passenger Origin 3,2% 2,4% 1,2% 0,4% 0,8% 1,6% 2,0% 2,8%
Notes: Jules

## Slide 37: Ground Access Mode
Notes: Jules

## Slide 38
LAX
Notes: Jules

## Slide 39
ONT
Notes: Jules

## Slide 40
LGB
Notes: Jules

## Slide 41
SNA
Notes: Jules

## Slide 42
BUR
Notes: Jules

## Slide 43: Los Angeles Traffic
Notes: Jules

## Slide 44: Travel Time
LAX
BUR
ONT
Notes: Jules

## Slide 45: Travel Time Time Difference Best option : LAX
Notes: Jules

## Slide 46: Future Analysis
Particular emphasis will be placed on determining both cost of rescheduling and potential for fuel savings and carbon footprint reduction due to delay reductions.
We will begin to check the robustness of the scheduler to see if such a method is feasible under conditions of uncertainty.
Further refinement of the model to reflect real airspace conditions and Improvement of computation time efficiency
Notes: John

## Slide 47: Impacts of New Schedule
Time
Like most LA travelers, the passenger travels by car
Net ground travel time change: +/- 40 minutes
Reduced air delay: 3.1 min air (5.4 min block)
Net change for passenger 45.4 minutes less to 36.9 minutes more.
Money
The airline saves $2.30 on operating cost/passenger on block delay
The passenger spends +/- $2.94 on fuel
LAX landing fee and terminal concession revenue goes to BUR
Emissions
The airline reduces its carbon footprint by 1.65 lbs CO2/passenger
The passenger’s carbon footprint changes by +/- 19.7 lbs CO2
X passengers end up closer to their destination
Y passengers end up farther from their destination
A theoretical passenger lives somewhere between LAX and BUR, and flies to BUR instead of LAX (assuming Boeing 737-800)
The Big Question: How many passengers on that flight will end up closer to vs. farther from their destination?

## Slide 48: Implementation
Air travel to/from LA Area would be similar to pre-deregulation
  Government or other governing body regulates frequency of flights, departure times, and destination airports
Many entities involved:
  Nearly all domestic airlines and some international airlines
  LA Area airports, and all airports with non-stop service to this region
  The FAA and Air Traffic Controllers
  Federal, state and local governments
  Local communities
  International communities
Notes: Jerry

## Slide 49: Incentives
The current free market minimizes costs to all entities
Any disruptions will come at costs to at least some users:
  Costs of increased ground/road travel time and pollution
  Costs of more complex international connections
  Costs of reduced airline and airport revenue
  Psychological costs associated with loss of convenience
Existing incentives:
  More efficient airside travel experience
  Reduced aircraft operating costs and pollution
Some individuals may not accept any incentives at all
Notes: Jerry

## Slide 50: Pros
Reduced emissions
Better passenger experience
Possible cost savings
A better utilized system
Reduced ground traffic
Possible increased profits for airlines
Time savings!
… but for the air and airport taxiways
Notes: Jack

## Slide 51: Cons
Changing from the norm
Rerouting flight paths
Passengers could be resistant to change
Increased traffic at 4 airports other than LAX
Loss of profit for LAX
Might not be a demand for rerouted flights
Notes: Jack

## Slide 52: Summary
Background research on the LA airport markets
Obtained data from ASPM and Google Maps
Visualized both data sets
Optimized and analyzed data
Outline implementation of our proposed solution
Notes: Everyone